## Slide 1: Modelling customisation and implementation report
Fred F. Hattermann et al., Potsdam Institute for Climate Impact Research

## Slide 2: Outline
Outline
Introduction
Fast-track information on climate change and impacts streamlined to the demonstrators
Advanced climate scenario data and bio-physical modelling implementation
Web portal for data and information
Conclusions and outlook

## Slide 3: Objectives
Research aims and questions of this deliverable (D2.2)
To provide information on climate change and climate change impacts on bio-physical indicators streamlined to demonstrators of TransformAr
To upscale impacts and possible adaptation measures to the EU scale with high-resolution
Main partners: CMCC, ACTERRA, NCSRD, Demonstrators

## Slide 4
However, in the course of the project, it turned out that the demonstrators had a demand for climate scenario and climate impact information from the start, while the deliverable D2.2 is due in month 36.
Also, it became obvious that the partners and end users had problems to understand the nature, underlying assumptions and amount of data available for them, although support was granted by PIK, CMCC and other involved partners. The data availability and description were also a demand from the midterm review.
The updated objectives of Deliverable 2.2 are therefore:
To provide climate and climate change impacts on bio-physical quantities streamlined to demonstrators throughout the project from its early phases (feeds into D2.1)
To support demonstrators in their workshops and products with information and presentations on climate change risks and related impacts in their region
To upscale impacts and to support design of possible adaptation measures to the EU scale with high resolution
To visualize and make available the data and information via an easy to use web portal

## Slide 5: Outline
Outline
Introduction
Fast-track information on climate change and impacts streamlined to the demonstrators
Advanced climate scenario data and bio-physical modelling implementation
Web portal for data and information
Conclusions and outlook

## Slide 6: Model approach fast track
3 scenarios (low end, medium and high end warming) with 10 global climate model outputs each of the latest scenario generation (CMIP6)
The data were statistically downscaled and bias adjusted within the ISIMIP project
An eco-hydrological model was applied to translate the climate scenario data into change in water resources and extremes

## Slide 7: Temperature Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Temperature
Data: ISIMIP 3b
warm
cold
Climate Models
x
Emission scenarios
Emission scenarios
Possibly very strong temperature increase over 21st century relative to current conditions.
Increase depends much on the emission scenario → Time for action!
Notes: Data: https://www.isimip.org/ Phase 3b based on 5 Global Circulation Models (GCMs) of the CMIP 6 family which were used for the latest IPCC report (AR6).
3 emission scenarios (as used in latest IPCC report, AR6):
- Purple line: SSP 1 RCP 2.6 (optimistic)
- Green: SSP 3 RCP 7.0 (business as usual)
- Yellow: SSP 5 RCP 8.5 (pessimistic)

## Slide 8: Temperature Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Temperature (2031-2060)
Data: ISIMIP 3b
warm
cold
Climate Models
x
Emission scenarios
Emission scenarios
Climate Models
x
Emission scenarios
Near future: + 1.5 °C.
Temperature increase stronger in winter (+ 2.3 °C in Jan) than in summer (+ 1.5 °C in Aug) here as well.

## Slide 9: Temperature Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Temperature (2071-2100)
Data: ISIMIP 3b
warm
cold
Climate Models
x
Emission scenarios
Emission scenarios
Climate Models
x
Emission scenarios
Far Future: + 2.7 °C
A high increase in winter temperature (+ 4.2 °C in Jan)
In summer the rise in temperature about + 2.4 °C
Uncertainty is also higher than previous time slices.

## Slide 10: Precipitation Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Precipitation
Data: ISIMIP 3b
dry
wet
Climate Models
x
Emission scenarios
Emission scenarios
Increase in rainfall projections.

## Slide 11: Precipitation Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Data: ISIMIP 3b
dry
wet
Precipitation (2031-2060)
Climate Models
x
Emission scenarios
Emission scenarios
Climate Models
x
Emission scenarios
Near future:
Strong increase in winter and spring rainfall (+ 7.6 % in Jan and 16.5% in Apr).
Decline in summer rainfall ~-2.9% in Jul

## Slide 12: Precipitation Projections – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Data: ISIMIP 3b
dry
wet
Precipitation (2071-2100)
Climate Models
x
Emission scenarios
Emission scenarios
Climate Models
x
Emission scenarios
Far future:
Similar pattern with high increase in rainfall in all seasons (+35% in Jan) except summer (-4.3% in Aug).
Higher uncertainty

## Slide 13: Trend in intense precipitation and surface runoff under high-end climate change conditions – Example 1
Trend increase in precipitation
Trend increase in surface runoff

## Slide 14: Trend in intense precipitation and surface runoff under high-end climate change conditions – Example 1
Trend increase in precipitation
Trend increase in surface runoff

## Slide 15: Health and heat
Health: Wet Bulb Globe Temperature
Workshop II: Egaleo – Climate vulnerability, Impacts and Projections
Wet Bulb Globe Temperature (WBGT) is a measurement used to assess the risk of heat related illnessess due to exposure to the current temperature, humidity, wind speed and solar radiation parameters.
Max WBGT corresponds to the daily maximum values of WBGT.
< 25.6°C - 27.7°C = White: 5 min rest every 30 min
27.8°C - 29.4°C = Green: 5 min rest every 25 min
29.5°C - 31°C = Yellow: 5 min rest every 20 min
31.1°C - 32.1°C = Red: 5 min rest every 15 min
> 32.2°C = Black: Suspend athletic activities recommended

## Slide 16: Heat and outdoor productivity
Outdoor productivity
Workshop II: Egaleo – Climate vulnerability, Impacts and Projections
Labor productivity denotes the maximum potential work output achievable by an individual in a day. This measure is represented as a percentage (%) to indicate the proportion of work that can be achieved under current climatic conditions. It is mainly derived from the impact of heat on productivity, as exposure to heat stress tends to diminish the average worker's capacity to perform tasks efficiently.
There are 4 different levels of labor productivity levels, each corresponding to a certain amount of work intensity:
200W = Low intensity work
300W = Medium intensity work
400W = High intensity work
500W = Very high intensity work

## Slide 17: Projected climate changes for Gjovik relative to 1991-2020
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
Heat stress
Data: ISIMIP 3b
 | 2021-2050 | 2031-2060 | 2071-2100
summer days (Tmax > 25 °C): | +103% (17 – 180%) | +146% (21–300%) | 366% (36 –1267%)
frost days (Tmin < 0 °C) | -12% (-26 – -6%) | -15% (-36 – -4%) | -28% (-70 – 6%)
icing days (Tmax < 0 °C) | -14% (-29 – -7%) | -19% (-39 – -4%) | -32% (-83 – 8%)
warm spells (at least 6 consecutive days with very high temperatures) | 185% (73 – 473%) | 231% (116 – 753%) | 548% (661 – 1695%)
cold spells (at least 6 consecutive days with very low temperatures) | -62% (-92 – 50%) | -69% (-96 – 0%) | -86% (-100 – -19%)

## Slide 18: Summary – Example of Gjovic
Workshop II: Gjovik – Climate vulnerability, Impacts and Projections
According to projections, Gjovik is likely to deal with
>
Milder winters
The increase of average temperatures will depend on emissions
Wetter Winters but with less snow
Overall precipitation increase

## Slide 19: Outline
Outline
Introduction
Fast-track information on climate change and impacts streamlined to the demonstrators
Advanced climate scenario data and bio-physical modelling implementation
Web portal for data and information
Conclusions and outlook

## Slide 20: Advanced model set-up
IMAGE
Multisite, multivariate stochastic weather generator
CaMa Flood
Hydraulic model
BN-FLEMOps
Probabilistic flood loss model
SWIM
Hydrological model
CORDEX-EU
Imperial College London
PIK Potsdam
PIK Potsdam
GFZ Potsdam
  GCM-RCM climate model simulations
Advanced model set-up

## Slide 21: Eco-hydrological model SWIM
Weather / climate (input)
  Precipitation (rain & snow)
  Temperature, solar radiation, rel. humidity
Hydrology
  Infiltration
  Runoff: surface, sub-surface, groundwater
  River discharge
  Evapotranspiration
Vegetation
  Natural: forests, grasslands, savannah...
  Managed crops
Glaciers
Natural processes

## Slide 22: Eco-hydrological model
Water and land management
Crop management
  Crop rotations
  Fertilization
Irrigation
  Crop water demand / deficits
  Water use efficiency
Water allocation
Reservoirs
  Hydropower
  Flood protection
  Water supply

## Slide 23: Spatial data
European Soil Map
CORINE land use map
Digital Elevation Model of 100 m resolution
Climate data of European Weather Service
ISIMIP climate scenario data
Basic GIS layers
Hydrotopes (HRUs)
Elevation, slope (DEM)
Land use / cover (LULC)
Soils
Other
Natural, managed
Reservoirs, irrigation,
wetlands, glaciers, elevation
Climate input

## Slide 24: Model implementation
28 River regions
Divided into 3100 subbasins
~ 1200 Gauge stations

## Slide 25: Model implementation
DEM 100 m
Land us CORINE 2020
European Soil Map

## Slide 26: Model implementation
Statistical results > 0.5 is “good”
Model result evapotranspiration

## Slide 27: Model results
Model result change in annual max flow
Model result change in annual GWR

## Slide 28: Model result CaMa-Flood
Observed and simulated inundation

## Slide 29
West Country
Impacts on water availability, vegetation and extremes

## Slide 30: Example: West Country
No of catchments: 344 No of subbasins: 1630
No of hydrotopes: 47948
No. of discharge station: 167

## Slide 31: First step: Investigation of observed discharge (River Exe)
Daily discharge River Exe [m3/s]
Return period [a] Discharge [m3/s]
5 161.5
10 184.8
25 214.2
50 236.0
100 257.7
250 286.2
Observed discharge and extremes (River Exe)
Flood statistics

## Slide 32: River Exe, development of river discharge
Trend in annual discharge (River Exe)

## Slide 33: Comparison of observed and modeled discharge
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
SWIM was applied for 344 river catchments in GB, including 4 located in Westcountry:
River Tamar
River Torridge
River Taw
River Exe
(Global multi-goal calibration using observed discharge at XYZ stations and sattelite ET data)
Example: River Exe – modelled and observed discharge [m3/s]

## Slide 34: Projected annual and seasonal discharge (River Exe)
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Development of annual discharge until end of the century (River Exe)

## Slide 35: Projected annual and seasonal discharge (River Exe)
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Development of monthly discharge (River Exe)
Development of monthly discharge (River Tamar)

## Slide 36: Development of flood hazard – hot scenario
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Exe – change in flood return levels high end scenario
Strong increase in flood risk mid – end of century
Projected changes in flood hazard (River Exe) – hot scenario RCP585
More
More
often

## Slide 37: Development of flood hazard – green scenario
Projected changes in flood hazard (River Exe) – green scenario RCP126
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Exe – change in flood return levels high end scenario
After increase until mid of the century a slow decrease in flood hazard
River Exe – change in flood return levels low-end scenario

## Slide 38: Development of flood hazard – hot scenario
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
River Tamar – change in flood return levels high-end scenario
Strong increase in flood risk mid – end of century
Projected changes in flood hazard (River Tamar) – hot scenario RCP585

## Slide 39: Development of flood hazard – green scenario
Projected changes in flood hazard (River Tamar) – green scenario RCP126
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
After increase until mid of the century a stronger decrease in flood hazard
River Tamar – change in flood return levels low-end scenario

## Slide 40: Change in hydrological processes at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Soil water flows and vegetation growth (arable land)
1971-2000
2071-2100
precipitation

## Slide 41: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Surface runoff
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 42: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Groundwater recharge
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 43: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Evapotranspiration
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 44: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 45: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Soil water
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 46: Change in hydrological porcesses at plot scale
Workshop II: Westcountry – Climate vulnerability, Impacts and Projections
Leaf Area Index
Water stress
Soil water
Soil water flows and vegetation growth
1971-2000
2071-2100

## Slide 47
Impacts on water quality

## Slide 48: Impacts on water quality
Change in nutrient flows (total nitrogen):
Past: High losses in winter with percolation
Losses
Plant uptake
Very management dependent
Second crop? Fertilizer regime?
Cover crops are relevant

## Slide 49: Crop modelling
Cumulative yield change (%) at NUTS2 level in 2030 and 2050 following ssp1.26 and ssp5.85 emission scenarios. The yield change refers to the weighted sum of maize, potato, rice, sorghum, soy and winter wheat yields

## Slide 50: Data provision beyond demonstrator process
For example to D2.6:
Groundwater recharge and water yield as indicator for risk for water security
Max annual flood as an indicator for flood risk
Climatic Water Balance as an indicator for drought risk
Wet Bulb Globe Temperature as indicator for health risk
Outdoor productivity and crop yields as one indicator for economical risk
Many other (temperature, precipitation etc)
All converted to Nuts2

## Slide 51: Outline
Outline
Introduction
Fast-track information on climate change and impacts streamlined to the demonstrators
Advanced climate scenario data and bio-physical modelling implementation
Web portal for data and information
Conclusions and outlook

## Slide 52: Web portal for data and information
https://kfo.pik-potsdam.de/eur/index_en.html?language_id=en
https://kfo.pik-potsdam.de/eur/index_en.html?language_id=en

## Slide 53
Summary
Fast-track information on climate change and impacts streamlined to the demonstrators Ready
Advanced climate scenario data and bio-physical modelling implementation Far but ongoing
Web portal for data and information Version 1 ready but ongoing

## Slide 54
Thanks!
Any questions?